## Slide 1: Investigating CTEV (Clubfoot) Orthosis through Re-design, Automation and Alternative Mechanism
DURATION – 01TH AUG, 2022 TO 13TH MAY, 2023
Submitted By: Group-P2
Ananya Maheshwari-2019UME1218
Mohit Khemchandani-2019UME1246
Shailesh Suthar-2019UME1168
Supervisor: Dr. Harlal Singh Mali
Associate Professor Department of Mechanical Engineering
MNIT, Jaipur
FYP’2023

## Slide 2: CONTENTS
Introduction to CTEV
Prior Efforts in CTEV Clubfoot Orthosis
Assembly Video: Worm and Worm Gear Mechanism
Introduction
  Objective
  Technical issues identification in existing clubfoot orthosis
  Technical issues rectification in existing clubfoot orthosis
  Prototype development of Forefoot of Orthosis
  Prototype development of Hindfoot of Orthosis
Automation in Existing Clubfoot Orthosis
  Automation in existing clubfoot orthosis
  Hardware and software requirement
  Root development of clubfoot
  2DOF linkage mechanism
  3DOF linkage mechanism
  6DOF linkage mechanism of Orthosis
Alternate locking mechanism
  Alternate locking mechanism
  Mechanism selection
  Working mechanism
  Prototype development
Conclusion and Future Scope
Thank-you

## Slide 3: Background understanding

## Slide 4: INTRODUCTION TO CTEV
Congenital Talipes Equinovarus also known as Clubfoot, is a complex, congenital deformity in which the foot is twisted out of shape.
Our objective is to develop a corrective orthosis for this disease which can be worn by the new-born child.
The major requirements of this orthosis are that it should be of low cost and weight so that anyone can afford it and can be worn by the child comfortably
Earlier for rectifying this kind of deformity into the new born baby we were using Ponseti Method.
Fig.1 Deformities in Clubfoot
Fig.2 Ponseti Method

## Slide 5: PRIOR EFFORTs
2019
2020
2018
2021
Fig. 1‑9 (a) Interference Indexing Mechanism (b) Nut and Bolt indexing mechanism (c) Friction locking mechanism Worm-Gear (d) Friction locking mechanism with metallic seating for worm gear placement.

## Slide 6: ASSEMBLY VIDEO: WORM & WORM GEAR MECHANISM

## Slide 7: TECHNICAL ISSUES IDENTIFICATION IN CLUBFOOT ORTHOSIS
7
Too small parts
Low precision
Manufacturing
Shrinkage was high during investment casting
Actuation
Very costly and time consuming
Cost & time

## Slide 8: OBJECTIVE
Re-design the clubfoot orthosis to rectify the criticality into an actuation which actuated using worm and worm gear mechanism.
Investigating the scope of automation in clubfoot using MATLAB.
Re-design the clubfoot orthosis to incorporating alternate locking mechanism of motion.

## Slide 9: TECHNICAL ISSUES RECTIFICATION IN EXISTING CLUBFOOT ORTHOSIS
Standard worm and worm gear
Swadeshi Gear manufacturer
Made by CNC
Customised worm and worm gear
Made by investment casting
Accepted
Rejected

## Slide 10: TECHNICAL ISSUES RECTIFICATION IN EXISTING CLUBFOOT ORTHOSIS

## Slide 11: TECHNICAL ISSUES RECTIFICATION IN EXISTING CLUBFOOT ORTHOSIS

## Slide 12: PROTOTYPE DEVELOPMENT OF FOREFOOT OF ORTHOSIS
Iteration-1
Iteration-2
Iteration-3
Iteration-4
CAD Model with exact dimension
CAD Model with Shrinkage allowances
Addition of Filling allowances
encountering filling allowances with shrinkage allowances
Final Design

## Slide 13: PROTOTYPE DEVELOPMENT OF HINDFOOT OF ORTHOSIS
Iteration-1
Iteration-2
CAD Model with exact dimension
Encountering filling allowances with shrinkage allowances

## Slide 14: AUTOMATION IN EXISTING CLUBFOOT ORTHOSIS

## Slide 15: AUTOMATION IN EXISTING CLUBFOOT ORTHOSIS
Children having Clubfoot problem
Wearing mechanical type orthosis
Go to the doctor for weekly check-up and monitoring the orthosis
Excessively laborious
Time-consuming
AUTOMATION
Next level

## Slide 16: HARDWARE AND SOFTWARE REQUIREMENT
Software:
  MATLAB & Simulink
  Inventor & OnShape: for building the assembly of clubfoot and integrate with MATLAB
Hardware:
  Stepper motors: getting installed on each pivot point of clubfoot
  Arduino
  Jumper wires
  Battery
  Breadboard

## Slide 17: ROOT DEVELOPMENT OF EXISTING CLUBFFOT ORTHOSIS
In which we will integrating stepper motor at each pivot point which were previously actuated using a worm and worm gear mechanism.
An automated orthosis would be able to make an accurate prediction of the trajectory along which the deformed foot would eventually revert to its original shape.
To do this, we used MATLAB to plot out the predictable path or a trajectory that orthosis should follow.
2 DOF Mechanism
3 DOF Mechanism
6 DOF Mechanism
Orthosis

## Slide 18: LINKAGE MECHANISM: 2DOF
Assembly Creation
Forward Kinematics

## Slide 19: LINKAGE MECHANISM: 2DOF
Inverse Kinematics

## Slide 20: LINKAGE MECHANISM: 3DOF
Assembly Creation
Forward Kinematics

## Slide 21: LINKAGE MECHANISM: 3DOF
Inverse Kinematics

## Slide 22: LINKAGE MECHANISM OF ORTHOSIS: 6DOF
Assembly Creation

## Slide 23: LINKAGE MECHANISM OF ORTHOSIS: 6DOF
Forward Kinematics
PD Controller Tuning
Input Signals

## Slide 24: LINKAGE MECHANISM OF ORTHOSIS: 6DOF
Forward Kinematics

## Slide 25: LINKAGE MECHANISM OF ORTHOSIS: 6DOF
Inverse Kinematics

## Slide 26: ALTERNATE LOCKING MECHANISM

## Slide 27: ALTERNATE LOCKING MECHANISM
The manufacturing of worm and gear is a very expensive process
mainly due to its very small size and specialized manufacturing techniques and setups involved.
Quality control process also add to this cost.
This would make the orthosis unaffordable and out of reach for certain group of people.
Thus, a need arises to look for different mechanism to lock the degrees of freedom of the orthosis.
The aim is to look for mechanism which can be assembled easily while using standard off-the-shelf products or those which can be easily manufactured, without heavy setup.
27

## Slide 28: MECHANISM SELECTION
28
Mechanism |  | Pros | Cons
2 Pin Mechanism |  | Uses very simple components which are easily manufacturable. | Low resolution Cannot withstand high forces as contact area is small.
3 Gear Mechanism |  | Has a very high resolution Reliable and can withstand high forces. | Complicated assembly. Position of gears cannot be calculated.
Fastening Mechanism |  | Very simple assembly No specialized parts required. Has infinite resolution | Poor reliability Position may gradually change due to jerks and impacts Cannot withstand high forces.

## Slide 29: THREE GEAR DESIGN AND CALCULATIONS
29
Pitch diameter (D) | 6.6666 mm
Diametral pitch (P) | 3.0002
Circular pitch (CP) | 1.047 mm
Module (m) | 0.3333 mm
Addendum (a) | 0.1667 mm
Dedendum (b) | 0.4166 mm
Working Depth (h) | 0.7499 mm
Tooth Thickness (t) | 0.5235 mm
Fig. 4‑4 Spur Gear with 3mm Hole

## Slide 30: WORKING MECHANISM
Since manufacturing of worm and worm gear along with automation is too costly.
Thus to make the orthosis cheaper, we need to look at some other less costly mechanism to lock the rotation.
30

## Slide 31: ASSEMBLY VIDEO
31

## Slide 32: PROTOTYPE DEVELOPMENT
First, a fixture was designed to test out if the proposed mechanism will work or not.
The fixture is 3D printed along with the gears.
Positive outcome of the fixture promoted us to design the complete orthosis assembly with the new ‘3 Gear’ mechanism.
Since off-the-shelf
Fig. Prototype for Yawing motion
Fig. Fixture for stability of 3 gear mechanism (i) CAD design (ii) SLA Printed Fixture

## Slide 33: CONCLUSION

## Slide 34: CONCLUSION AND FUTURE SCOPE
The primary objective of this final year project was to improve functionality of the existing orthosis and investigating the scope of implementing automation.
Parallel to investigation of automation and development of the orthosis with alternate mechanisms was also done.
The alternate mechanisms explored were such that their manufacturing, quality assurance, testing and assembly were much cheaper compared to the existing worm and gear assembly.
Although efforts have been made to improve the orthosis by including automation and looking for alternate mechanisms, it is still not ready to be used, and has much room for improvement.
The future work may include developing the orthosis prototype incorporating the hardware for orthosis automation, which includes procurement of items such as stepper motors, sensors, IDE, battery packs, etc, after which design changes may be done to incorporate these sensors and motors in the orthosis.
Further, integration of work on MATLAB Simulink with the hardware is necessary.
34

## Slide 35: CONTRIBUTION
Existing Orthosis Re-Design
Automation in Clubfoot
Alternate Locking Mechanism
Mohit Khemchandani
2019UME1246
Shailesh Suthar
2019UME1168
Ananya Maheshwari
2019UME1218